## Slide 1
Nexora Network Infrastructure Initiative
CCNA Capstone Project — Design, Build & Secure an Enterprise Network
Nexora Technologies LTD
Prepared by: Kibet Jerop Annette
October 2026

## Slide 2
Scenario & Objectives
Nexora Technologies Ltd.
A mid-sized technology and digital solutions company operating from a Head Office in Nairobi and a Branch Office in Eldoret. Leadership asked for:
Departments kept logically separated
Reliable routing between the two offices
Unauthorized devices and rogue DHCP blocked
Remote device management restricted to IT staff
Separate Departments
Each department gets its own private network, kept apart from the others
Connected Offices
The two offices are linked so they work as one company
Controlled Access
Rules and checks stop unknown devices from joining the network
IT-Only Management
Only IT staff can log in to manage the network equipment

## Slide 3
How We Built It
1 Design
Planned the departments, the address scheme and the layout before touching any equipment.
2 Build
Connected the offices, set up routing, backup routers and automatic addressing.
3 Secure
Added guest isolation, access rules, device lock-down and rogue-device protection.
4 Test
Proved each feature works by breaking things on purpose, like switching off a router.
Notes: Walk through the four stages in order. Stress that testing was deliberate: we tried to break the network to prove it recovers.

## Slide 4
Network Topology
Head Office — Nairobi
R1 (Active)
R2 (Standby)
SW1
SW2
Two switches linked by two cables
Two routers: one main, one backup
Branch Office — Eldoret
R1 (Active)
R2 (Standby)
SW1
SW2
Two switches linked by two cables
Two routers: one main, one backup
WAN Link
(between offices)
Routers direct traffic and switches connect the devices. Each office has two of each, so one can cover for the other.

## Slide 5
Each Department, Its Own Network
VLAN | Gateway (HQ / Branch) | DHCP Range
10 - Sales | 10.10.10.1 / 10.20.10.1 | x.x.4-14
20 - Operations | 10.10.20.1 / 10.20.20.1 | x.x.4-14
30 - IT | 10.10.30.1 / 10.20.30.1 | x.x.4/5-14
40 - Management (HQ) | 10.10.40.1 | x.x.4-6
50 - Guest | 10.10.50.1 / 10.20.50.1 | x.x.4-6
99 - Network Mgmt | 10.10.99.1 / 10.20.99.1 | x.x.4-6 (static)
11
Separate networks, sized to fit
Bigger networks for bigger teams
Smaller ones for Management,
Guest and network equipment
Think of each VLAN as a department's private street. Addresses are handed out automatically and sized to fit each team, with room to grow.

## Slide 6
Reading an Address: 10.20.30.2
10
Company network
Every Nexora address starts here: private, inside the company.
20
Which office
10 = Head Office,
20 = Branch.
30
Which department
Matches the VLAN: 10 = Sales, 20 = Operations, 30 = IT.
2
Which device
1 = shared gateway, 2 = main router, 3 = backup router, 4 and up = devices.
Notes: Use the street-address analogy: country, city, street, house number. Each part of the address answers a question.

## Slide 7
End Devices
Site | Department | Devices
Head Office | Sales | PC, Shared Printer*
Head Office | Operations | PC
Head Office | IT | PC, Laptop, File Server
Head Office | Management | PC
Head Office | Guest | Wireless Laptop (via AP)
Branch Office | Sales | PC, Shared Printer*
Branch Office | Operations | PC
Branch Office | IT | PC
Branch Office | Guest | Wireless Laptop (via AP)

## Slide 8
How the Offices Talk: Routing
One WAN link
A single dedicated connection joins Nairobi and Eldoret..
A shared map (OSPF)
Every router tells its neighbours what it can reach, so each one learns the route to every department in both offices.
Self-updating
If a path changes, the routers update their map automatically. Nothing is re-entered by hand.
Notes: Routers are like drivers sharing a live road map. OSPF is the name of the method they use to share it.

## Slide 9
Redundancy: HSRP & EtherChannel
Backup Router (HSRP)
Each office has two routers sharing one address, like a duty-desk phone number. If the main router fails, the backup answers the same number within seconds and nobody has to change anything.
Double Cable (EtherChannel)
Two cables between each office's switches work as one wide road. If one cable is cut, traffic keeps flowing on the other with no interruption.
Notes: Optional: one failover screenshot, or run the live demo. Plain-language point: the backup takes over and users notice nothing.

## Slide 10
Security Implementation
Port Security
Each wall socket accepts only its registered device. A stranger's laptop is blocked and logged.
DHCP Snooping
Stops a fake address-giver from misdirecting devices. Only the real one is trusted.
SSH & Hardening
Encrypted remote login only, scrambled stored passwords, and a warning banner on every device.
Access Rules (ACLs)
Visitors can't reach company data, and only IT staff can log in to manage equipment.
Notes: Optional: one annotated failed-ping screenshot. Plain-language point: a visitor can use the network but cannot reach company systems.

## Slide 11
Guest Network
What visitors get
They join the Nexora-Guest Wi-Fi and receive an address automatically, in their own private network, separate from every department.
What visitors cannot do
Reach any department, the file server or the printers. Rules on the routers block that traffic in both directions.
Proven in testing: a guest laptop's pings to company devices failed, and company devices could not reach the guest either.
Notes: This mirrors a real office guest Wi-Fi: visitors are kept apart from company systems.

## Slide 12
Automatic Addresses: DHCP
DISCOVER
The pc broadcasts a request asking for a DHCP server.
→
OFFER
R1 offers the pc an available IP address
→
REQUEST
The PC requests the offered address.
→
ACKNOWLEDGE
R1 confirms the lease, and the PC can use the address
The shared gateway, the two routers, the file server and the network equipment keep fixed addresses so they can always be found. Everything else, such as PCs and laptops, takes whatever is free, so no one has to type an address by hand.
Notes: DHCP is the hotel front desk handing out room numbers. Staff who need a permanent room, like the file server, are given one in advance.

## Slide 13
Key Terms
Term | In plain words
VLAN | A private network for one department, like a separate floor of the building
Router / Switch | Router = traffic director between networks. Switch = connects devices within one network
HSRP | Two routers share one address so a backup takes over instantly, like a duty-desk phone
EtherChannel | Two cables working as one wide road, so losing one doesn't stop traffic
OSPF | How routers share a live map so traffic always finds a path between offices
ACL | A guest list for the network: who may reach what

## Slide 14
Thank You
Questions?